1. Vision part
  1. GoPro Hero4 as the main camera
  2. The range is 5-10 meters with drone’s WiFi, up to 40-50 meters (if it wants)
  3. Video resolution for now: 432 x 240
  4. Camera’s delay is approximately 1 sec
  5. Library used - OpenCV
  6. The videos stream comes in FFMPEG codec
  7. Video is processed on laptop (Intel i5, NVIDIA 640M, 6 GB RAM)
  8. cv2.resize if not used (resolution is low already)
  9. Trackers:
    1. MIL - high FPS, easy to lose target, previous position dependent
    2. TLD - resources hungry tracker, but tracks and finds objects rather robustly
    3. MEDIANFLOW - great tracking, high FPS, no recovery after losing the object
  10. After determining the object, it subtracts the middle point and sends it to the controller computer
    1. The tracker makes a bounding box
    2. The tracked point is the centre of bounding box
  11. Communication between computers is organized via cable using socket
2. Control part
  1. General
    1. The drone flies only outdoors (does not arm indoors in any mode)
    2. The computer control mode is GUIDED only
    3. Libraries used - dronekit, mavlink
    4. Control computer connects with the joystick via WiFI
      1. Protocol for connection - UDP
    5. Joystick receives commands and send control to quadrotor
  2. Controller computer implements keyboard control
    1. simple_takeoff and landing mode work clearly
    2. YAW and VELOCITY(X,Y,Z) work by compass only
      1. if X>0 - quad goes North
      2. if X<0 - quad goes South
      3. if Y>0 - quad goes EAST
      4. if Y<0 - quad goes West
    3. Implemented relative positioning using projections (details in another doc)
    4. Implemented YAW using mutable state
    5. Library for keyboard listening - pynput
  3. Controller computer implements tracking control
    1. The drone tries to hold the tracked object in the middle
    2. The holding is implemented with VELOCITY(X,Y,Z) function, where X,Y are projections to coordinates (do not forget that drone is positioned by compass!)
    3. The velocity is raised proportionally according the distance between center of view and the tracked object
      1. The set maximum speed depends on the tracked object maximum speed
  4. If the object is lost, drone waits for the manual determining the object
    1. The tracker can find the object (TLD, for instance), start tracking the environment (MIL) or stop working/behave indefinitely (MEDIANFLOW)

System overview:

Controller program structure